## Slide 1
🌱 SMART GREENHOUSE MONITORING SYSTEM
Automated Real-Time Telemetry, Plant Analytics & Closed-Loop Anomaly Control
Flow: Sensors ➔ Database ➔ Data Analytics ➔ Anomaly Detection ➔ Hardware Output

## Slide 2
Project Overview & 5-Stage Architecture
Architecture
⚠️ The Horticultural Challenge
• Uncontrolled climate swings (heatwaves, cold snaps) severely stunt plant growth.
• Excessive humidity fosters mold, mildew, and fungal outbreaks.
• Stale air and CO2 depletion stall photosynthesis, reducing crop yield.
• Manual inspection is slow, labor-intensive, and prone to human error.
• Need: An automated 24/7 closed-loop monitoring & protection system.
⚡ The 5-Stage Solution Flow
• Stage 1 (Sensors): Physical acquisition via ESP32, DHT22, LDR, MQ-135.
• Stage 2 (Database): Ingestion via Flask REST API into SQLite database.
• Stage 3 (Analytics): Calculating VPD, CO2 availability, and Oxygen balance.
• Stage 4 (Anomalies): Multi-parameter rule checks and severity scoring.
• Stage 5 (Hardware Output): Closed-loop relay triggers and live Streamlit UI.

## Slide 3
Stage 1: Sensor Data Acquisition (Edge Layer)
Stage 1: Sensors
🔌 Hardware Sensors & Pinouts
• DHT22 / DHT11 (GPIO 4): Temperature (°C) & Relative Humidity (%).
• LDR Light Sensor (GPIO 34): Solar light converted to Lux (lx).
• MQ-135 Gas Sensor (GPIO 35): Air quality converted to AQI (Index).
• 12-bit ADC (0 - 4095 counts): High-resolution analog voltage digitization.
• Onboard Status LED (GPIO 2): Real-time WiFi & transmission indicator.
📡 Signal Processing & WiFi Transmission
• Hardware Signal Smoothing: Multi-sample averaging reduces noise.
• Unit Conversion Engine: Non-linear mapping from ADC to Lux and AQI.
• Structured JSON Payload: Formatted with temperature, humidity, light, gas.
• HTTP POST /data: Transmitted to Flask backend over WiFi every 2-3s.
• Auto-reconnection logic: Ensures continuous telemetry streaming.

## Slide 4
Stage 2: Ingestion & Database Management
Stage 2: Database
🚀 Flask REST API Backend
• Listens on port 5000: Handles high-throughput sensor telemetry.
• Endpoint POST /data: Ingests packets and returns immediate anomaly state.
• Query Endpoints: /latest, /history, /stats, /anomalies, and /health.
• CORS Enabled: Supports direct integration with dashboards & web apps.
• Thread-Safe Connection Pooling: Robust multi-client query handling.
💾 ACID-Compliant SQLite Database
• Database File: backend/greenhouse.db with structured table sensor_data.
• Schema: (id, timestamp, temperature, humidity, light, gas).
• High-Precision Timestamps: ISO-8601 UTC timestamps on every row.
• Fast B-Tree Indexing: Instant time-series lookups and chronological ordering.
• Historical Integrity: Clean persistent storage for offline data analytics.

## Slide 5
Stage 3: Data Analytics & Plant Physiology
Stage 3: Analytics
🌿 Botanical Feature Engineering
• Vapor Pressure Deficit (VPD in kPa): Quantifies plant transpiration.
• Optimal Sweet-Spot (0.8 - 1.4 kPa): Maximum photosynthesis without wilting.
• CO2 Availability (ppm): Tracks carbon assimilation for crop biomass.
• Oxygen (O2 %) Dynamic Balance: Balances day photosynthesis & gas displacement.
• Dew Point Temperature (°C): Predicts leaf condensation and mold hazard.
📈 Statistical Insights & Trends
• ETL Pipeline (prepare_data.py): Automatic cleaning and physical sanity bounds.
• Pearson Correlation Analysis: Discovers temp-humidity inverse relationships.
• Descriptive Statistics: Mean, std deviation, min/max, quartiles across time.
• Predictive Forecasting (Holt's Method): Projects trend 15-30 min ahead.
• Early Warning: Warns operators before environmental setpoints breach.

## Slide 6
Stage 4: Intelligent Anomaly Detection
Stage 4: Anomalies
🚨 Multi-Parameter Rule Checks
• High Temperature Alert: Flags overheating conditions (Temp > 40°C).
• Air Quality / Smoke Spike: Flags hazardous gas accumulation (AQI > 150).
• Compound Agricultural Rules:
• - Heat Stress + Wilt: High Temp (> 35°C) + Dry Air (< 30%).
• - Fungal Outbreak: Warm Air (> 24°C) + High Saturation (> 85%).
• - Leaf Scorch: Excessive Solar Irradiance (> 55,000 lx) + High Temp.
🧠 Severity & Actionable Remediation
• Graded Severity: NORMAL (0/100) vs ANOMALY (60-100/100).
• Multivariate Mahalanobis ML Scoring: Detects subtle multi-sensor drift.
• Contextual Operator Checklists:
• - 'Activate evaporative cooling and misting nozzles.'
• - 'Turn on emergency exhaust fans to clear hazardous fumes.'
• - 'Deploy shade screens to protect foliage from photo-inhibition.'

## Slide 7
Stage 5: Hardware Output & Real-Time Dashboard
Stage 5: Output
⚡ Closed-Loop Edge Actuation
• HTTP Response Feedback: Backend sends anomaly flags back to ESP32.
• Relay Module Triggers: Automatically switches ON cooling fans or misting pump.
• Exhaust Ventilation: Purges stale air upon detecting CO2/AQI spikes.
• Visual & Audible Alarms: Hardware status LED and buzzers alert on-site staff.
• Automated 24/7 Protection: No human supervision required for rapid response.
🖥️ Streamlit Monitoring Dashboard
• Live Telemetry Grid: Temp (°C), Humidity (%), Lux (lx), AQI, CO2, O2, VPD.
• Threshold Setters (Sidebar): Customizable slider limits for all metrics.
• Interactive Altair Trend Charts: Area gradients & dashed threshold lines.
• Live Condition Cards: Color-coded health banners and action checklists.
• CSV Data Export: One-click historical data and anomaly report download.

## Slide 8
Project Summary & Impact
Conclusion
🏆 Key Accomplishments
• ✅ Complete End-to-End System: Functional from physical sensors to actuation.
• ✅ Real-World Standard Units: Temperature, Humidity, Lux, AQI, CO2, O2.
• ✅ Botanical Intelligence: Advanced VPD modeling for transpiration health.
• ✅ Configurable Thresholds: Live tuning sliders for any crop type.
• ✅ Production-Ready Architecture: Flask REST API, SQLite, and Streamlit.
🌱 Agricultural & Economic Value
• Crop Protection: Prevents irreversible heat stress, frost, and fungal disease.
• Yield Maximization: Maintains optimal CO2 and VPD transpiration sweet-spots.
• Resource Conservation: Minimizes unnecessary fan/water pump power usage.
• Scalability: Easily expandable to multi-zone commercial greenhouse facilities.
• Thank You! Q&A Session.